## Slide 1
The GUARDYAN code: a full core realistic nuclear power plant simuation
Dr. Légrády Dávid
GPU Monte Carlo reactor dynamics code: GUARDYAN
Tomographic Image Reconstruction (PET, CT)
Budapest University of Technology and Economics
Institute of Nuclear Techniques
Notes: Kutatási fázis
realisztikus rendszerek
célkitűzés
Teljes Szerkezet:
mit akarunk
ez mekkora truváj
GPU és minden hozadéka
+ technikák: Woodcock, adjungált fésülés, stb.
verifikáció és bencsmárkok
Eredmények: TR + Cd
Paks I

## Slide 2
The Team
Team Members:
Dr. Dávid Légrády (associate professor, scientific coordinator, Monte Carlo variance reduction, reactorphysics)
Gábor Tolnai (physicist, algorithm and code development, testing,..)
Tamás Hajas (PhD Student, noise analysis of TH coupling)
József Kópházi (associate professor, reactorphysics, deterministic and MC transport methods )
Márton Pukler (MSc student, Monte Carlo variance reduction, sampling)
Gergely Ferenczy (MSc student, variance estimation)
Elod Pazman (MSc student, TH coupling, cross section homogenization)
Mark Margoczi (MSc student, TH coupling, noise propagation)
Boglarka Babcsany (applications, benchmark comparison)
Budapest University of Technology and Economics (BME)
Former Team Members:
Dr. Balázs Molnár (former PhD student, MC variance reduction)
Máté Halász (adjoint professor, stochastic processes)
Hajna Takács (MSc student, first code version)
Ábel Bartik (BSc student, tallying on GPU’s)

## Slide 3
BME NTI
Budapest University of Technology and Economics (BME, since 1782), Hungary; Institute of Nuclear Techniques; www.reak.bme.hu
Nuclear education anda 100kW training reactor since 1971 – 50 year anniversary

## Slide 4
Current competitive disadvantages:
4 NVIDA 1080 ( 5th birthday)
1 NVIDIA RTX 3090, A4000, A6000
Wigner GPU cluster (Tesla’s)
Waiting for Komndor HPC access
Similar Codes:
dynTRIPOLI – CEA, France (CPU)
dynSERPENT – VTT, Finnland (CPU)
“Ultimate Fidelity” Monte Carlo nuclear reactor code for backing safety analysis
GPU Assisted Reactor Dynamic Analysis, http://awing.reak.bme.hu/GUARDYAN
BME Training Reactor
(50th birthday)
Current competitive advantages:
GPU
Works on Power Plant scale (only us so far!)
Has been verified with Power Plant measurement data (only us so far!)
GUARDYAN Overview

## Slide 5
GUARDYAN - Overview
Physics:
Independent particles (photons)
Free path along a straight line
Direction change at boundary crossing
Simple scatter law(s)
Rarely diffusion-type transport
A few material parameters
Neutron transport MC – GPU vs visual rendering
Visual Monte Carlo GPU Rendering
Neutron Transport Monte Carlo
Accuracy requirement:
Shold look realistic
Surfaces represented as triangles
Hardware:
A few registers
Simple precision arithmetics
RTX
Physics:
Independent particles (neutrons)
Free path along a straight line
Free flight follows exponential pdf
Difficult scatter laws (approx. 70 types)
Always interaction within the material
Few Gbyites of nuclear data
Accuracy requirement:
10pcm (10x10-5) error is already unacceptable
2nd to 3rd order bounding surfaces
0.0015cm (15um) difference may cause 20% power drop
Hardware:
Large amount of registers needed
Double precision arithmetics
RTX?

## Slide 6
Maintaing a chain reaction:
A bit of reactorphysics in laymen’s terms
Escape
Absorption
Fission
1 neutron to 1.001 neutron / generation, 1000 generations /second = 2.7 x power increase / second
700pcm of the population is “delayed neutron precursor”, neutrons emerge later: reactor control
Time dependent system
Immense precision is needed
0.001 = 100pcm (percent mille)
Notes: Elég jó-e?
Szakmailag a konkurrenciához képest – erről beszélünk sokat
ahhoz, hogy iparilag alkalmazható legyen – ezért jöttünk, ennek eldöntéséhez hangzanak el részletek
akadémiai környezet vagy céges környezet tud jól szolgáltatni? Cégest finoman felvetni

## Slide 7
conventional reactor physics solvers
Boltzmann Equatons: integrodifferntial equation with 6 independent phase space and 1 time dimension
Notes: Elég jó-e?
Szakmailag a konkurrenciához képest – erről beszélünk sokat
ahhoz, hogy iparilag alkalmazható legyen – ezért jöttünk, ennek eldöntéséhez hangzanak el részletek
akadémiai környezet vagy céges környezet tud jól szolgáltatni? Cégest finoman felvetni

## Slide 8
conventional reactor physics solvers
Solvers for time dependent reactor dynamics:
2 energy group diffusion (! Most used! ) – requires heavy data preprocessing by MC
Nodal finite differences /finite elements – requires heavy data preprocessing by MC
Modal finite differences /finite elements (rare)
Stepwise Static Monte Carlo
Dynamic Monte Carlo (new, past few years)
GPU use:
For MC mostly, rare
Notes: Elég jó-e?
Szakmailag a konkurrenciához képest – erről beszélünk sokat
ahhoz, hogy iparilag alkalmazható legyen – ezért jöttünk, ennek eldöntéséhez hangzanak el részletek
akadémiai környezet vagy céges környezet tud jól szolgáltatni? Cégest finoman felvetni

## Slide 9
Path Sampling
S varies with
Temperature
Density
Energy
GUARDYAN uses the Woodcock-method
Mean free path = 1/ S

## Slide 10
Constrictive Solid Geometry
Cells: Homogeneous material, defined by bounding surfaces and boolean operators
Surfaces: plane, cylinder, sphere, ...
Lattices: rectangular and hexagonal
Transformation: rotation matrices
Materials: by isotope composition
Universes
Input logic similar to MCNP, Serpent, OpenMC
<geometry>
<surface id="1" type="cz" transform="301" coeffs="40.000"/>
<surface id="2" type="c/z" coeffs="5.000 17.32 10.0"/>
<cell id="2" material="13" surfaces="1" universe="53"/>
<cell id="3" material="dead" surfaces="-2 -1" universe="58"/>
<cell id="4" surfaces="-1" fill="58" transform="4"/>
<transformation id="4" displacement="0.2 0.2 0.2"
rotation="300 210 -90 390 300 -90 90 90 0"/>
<transformation id="0" displacement="0 0 0"/>
<lattice id="58" type="hexx" dimension="9 9" pitch="0.1 0.1"
universes ="
58 58 58 58 58 58 58 58 58
58 58 58 58 53 53 53 53 58
58 58 58 53 53 53 53 53 58
58 58 53 53 53 53 53 53 58
58 53 53 53 53 53 53 53 58
58 53 53 53 53 53 53 58 58
58 53 53 53 53 53 58 58 58
58 53 53 53 53 58 58 58 58
58 58 58 58 58 58 58 58 58"
transform ="
0 0 0 0 0 0 0 0 0
0 0 0 0 4 4 0 0 0
0 0 0 4 4 0 0 0 0
0 0 4 4 0 0 0 4 0
0 4 4 0 0 0 4 4 0
0 4 0 0 0 4 4 0 0
0 0 0 0 4 4 0 0 0
0 0 0 4 4 0 0 0 0
0 0 0 0 0 0 0 0 0"
/>
</geometry>

## Slide 11
Path Sampling

## Slide 12
GUARDYAN Population Control
Population in near critical systems
After the 1st generation 60% dies, off-springs of the 40% stays (no escape, n=2.5)
After the 2nd generation 88% dies, 12% of original samples’s offsprings stay
After the 3rd generation 90% dies, 10% of original samples’s offsprings stay
…
100th generation: 95% dies, 5% of original samples’s offsprings stay
Analog calculation would result in
Few samples would produce large amount of samples: one GPU thread would launch huge amount calculations
Rest of the threads would be idle
Non-analog calculation devised:
Fission does not split trajectories, only weight change occurs
In time steps the population is “combed” to maintan equal number of parallel running threads
“Forced fission” to avoid large weight fluctuations

## Slide 13
Combing
Analog combing
w1
w2
w3
w4
...
wN-2
wN-1
wN
New weight: S (wi)/M
M
M-1
1
2
Non-analog combing
f+1 w1
f+2 w2
f+3 w3
f+4 w4
...
f+N-2wN-2
f+N-1wN-1
f+NwN
New weight: S (wi)/M/f+i
M
M-1
1
2
Vissza

## Slide 14
Analog population collapsing
Notes: Hasadási statisztika

## Slide 15
Population Control with delayed neutrons
Delayed neutrons hangling
largely differing time scales of prompt and delayed neutrons
in reality 10 000 x so many precursors as prompt neutrons
after 1000 generations the population becames 99.9% precursors, they maintatin the power
Complicated precursor handling: non-analog treatment is neaded
Notes: Mit tud a GPU, ebből mi következik, ez mire ad lehetőséget
nem analóg mintavételezés, fontos!

## Slide 16
Verification with Power Plant data
Paks Nuclear Power Plant Unit 4, Campaign 32, BOC
vodo-vodyanoi enyergeticheskiy reactor (Sowiet/ Russian type)
Water-cooled water moderated reactor
440/v213
Nominal power 440 MWe
Power uprating to 500 MWe
Rod Drop Experiment (RDE), routinely performed at each campaign start
Asymmetric rod gets stuck (the most important one)
Time dependent ex-core detector readings recorded
Before Wigner 8xA100: 4 weeks – 4 seconds, repeated ?4 times?
After Wigner 8xA100: 2 weeks, 12 seconds, 8 independent replica runs
-> Publication
Legrady, D. ; Tolnai, G. ; Hajas, T. ; Pazman, E. ; Parko, T. ; Pos, I.
Full Core Pin-Level VVER-440 Simulation of a Rod Drop Experiment with the GPU-Based Monte Carlo Code GUARDYAN
ENERGIES 15 : 8 Paper: 2712 , 17 p. (2022)

## Slide 17
193 surfaces
107869 cells
119 lattices
4516 universes
1657 materials
187 isotopes
Verification with Power Plant data

## Slide 18
Paks NPP, block 4, campaign 32, fully detailed caltulation
Verification with Power Plant data

## Slide 19
Verification with Power Plant data

## Slide 20
Verification with Power Plant data

## Slide 23
Verification with Power Plant data

## Slide 24
Videos come
Verification with Power Plant data

## Slide 25
Verification with Power Plant data
BEFORE Wigner 8xA100

## Slide 26
Verification with Power Plant data
AFTER Wigner 8xA100

## Slide 27
Verification with Power Plant data

## Slide 28
Variance distribution

## Slide 29
Variance distribution

## Slide 30
EURTOM Nuclear Innovation Prize

## Slide 31
Variance distribution
Efficiency losses:
50% of thread use
Almost NONE of the extra double precision arithmetic capacity utilized

## Slide 32
Thank you for listening!