## Slide 1
GPU-based iterative CT reconstruction
Tamás Huszár Zsolt Adam Balogh
Tamas.huszar@mediso.com Zsolt.Balogh@mediso.com
R & D Mediso Ltd.
20-21 May 2015 Budapest, Hungary
5th GPU WORKSHOP - THE FUTURE OF MANY-CORE COMPUTING IN SCIENCE
Notes: 1

## Slide 2
Computed Tomography
2

## Slide 3
3
CUDA
CUDA (Compute Unified Device Architecture)
A parallel computing platform and programming model invented by NVIDIA. It enables increases in computing performance by exploiting the power of the graphics processing unit (GPU).
Hardware
Kepler microarchitecture
GeForce GTX TITAN Z (compute capacity 3.5, memory 12 Gb, CUDA cores 5760)
GeForce GTX TITAN Black (compute capacity 3.5, memory 6 GB, CUDA cores 2688)
Maxwell microarchitecture
GeForce GTX 980 (compute capacity 5.2, memory 4 GB, CUDA cores 2048)
GeForce GTX TITAN X (compute capacity 5.2, memory 12 GB, CUDA cores 3072)
Notes: 3

## Slide 4
CUDA
CUDA framework
Wraps and hides CUDA functionality
Enables fast development
Features
  Smart Device selection
  Occupancy calculations
  Kernel launch
  Memory management
4

## Slide 5
CUDA
CUDA framework
Smart device selection
  GPU filters (available memory, display cards, …)
  Get connected displays with NvAPI
Occupancy calculations and kernel launch
  Calculate block size for highest occupancy
  Semi-automatic with CUDA 6.5 occupancy API
  Kernel launch macros to hide thread micromanagement
5

## Slide 6
6
CUDA
CUDA framework
Kernel configuration macros
  Use cudaFuncGetAttributes to find register and shared memory usage
  cudaOccupancyMaxPotentialBlockSize
  kernel info + data size  blockSize3D, gridSize3D
Kernel launch macros
  Sync / Async mode for debug
  Profiling / logging
Thread index calculator for the CUDA kernel program
  Easy indexing for 2D and 3D image arrays using block and grid configuration
  Kernels must avoid over-indexing
Notes: 6

## Slide 7
7
CUDA
CUDA framework / Example
Kernel launch:
ADD_CONF(myKernel, 512*512*256);
KERNEL_LAUNCH_ASYNC(
myKernel, config["myKernel"], dataSize, parameters, ...);
myKernel:
uint tid = index();
uint2 pos = getXY( tid, dataSize.width );
data[pos.x, pos.y] = ...;
Notes: 7

## Slide 8
8
CUDA
CUDA framework / Device memory allocation
Generalized datastructures for different types
  array, layered array, global memory, pitched memory
  1D, 2D, 3D
  float, double, …
  Transparent multi-GPU support
Examples:
template<typename T> DeviceMemoryArray2D<T>
template<typename T> DeviceMemoryLinear3D<T>
template<typename T> DeviceMemoryLayered3D<T>
Notes: 8

## Slide 9
9
CUDA
Dynamic memory allocation example
DeviceMemoryLinear3D<float> volume1(gpu1);
DeviceMemoryArray3D<float> volume2(gpu2);
volume2.copy(volume1);
instead of
cudaMemcpy3DParms parms;
memset(&parms, 0, sizeof(cudaMemcpy3DParms));
parms.srcPos = srcPos;
parms.dstPos = dstPos;
parms.srcPtr = make_cudaPitchedPtr(devPtr, pitch, x, y);
parms.dstArray = array;
parms.extent = extent;
parms.kind = cudaMemcpyDeviceToDevice;
cudaMemcpy3DAsync( &parms, 0 );
Notes: 9

## Slide 10
Iterative CT reconstruction
Iterative CT generations | 
1st generation | Filtered Back Projection
2nd generation | Image-space Iterative Reconstruction
3rd generation | Statistical Iterative Reconstruction
4th generation | Model-based Reconstruction
10

## Slide 11
FBP
Forward-projection
Back-projection
Projections
Start image
Iterated projections
Iterated image
Result
Iterative CT reconstruction
11

## Slide 12
12
Iterative reconstruction types
Algebraic reconstruction techniques (ART, SART, SIRT)
solving y=Ax, where y is sinogram data, A is system model
Statistical reconstruction methods (EM, ML) (I ~ Poisson +
Normal)
Model-based methods (go beyond modeling statistics of the
detected photons as Poisson distributed)
Iterative CT reconstruction
Notes: 12

## Slide 13
13
Maximalization of the conditional probability P( μ | y ),
where μ is the distribution of linear attenuation coefficients
y is the vector of transmission measurements.
Backprojection
is the value of pixel j,
is the measured sinogram along line i,
is the intersection length of projection line i with pixel j.
Iterative CT reconstruction
Notes: 13

## Slide 14
14
Reconstructed volume (FBP and iterative)
Iterative CT reconstruction
Notes: 14

## Slide 15
15
Advantages
image noise reduction
dose reduction
artifact reduction
Disadvantages
computation time (using GPU)
model complexity
software complexity, non-linear algorithms
Iterative CT reconstruction
Notes: 15

## Slide 16
16
Projector types (parallelization)
pixel-driven (ray-driven)
voxel-driven
distance-driven
Iterative CT reconstruction
Notes: 16

## Slide 17
Optimizations
  CPU vs. GPU
  Memory access patterns
    Coalesced access
    Texture memory vs. global memory
  Use float instead of double where possible
  Memory size
  Multi-GPU
Iterative CT reconstruction
17

## Slide 18
Chart: GPU vs. CPU
| GPU | CPU
 | 2.5529 | 130.3549
Measurements
Reconstruction speed
18

## Slide 19
Measurements
Chart: Global memory vs. Texture memory
| global memory | texture memory
 | 2.5529 | 2.3409
Reconstruction speed
19

## Slide 20
Measurements
Reconstruction speed
Chart: Float vs. double
| float | double
Titan Black | 2.5529 | 8.0058
Titan X | 2.3621 | 8.6125
20

## Slide 21
Measurements
Chart: GPU memory usage test
| Titan Black (6 Gb) | Titan X (12 Gb) | GTX 980 (4 Gb)
 | 133.3818 | 82.6715 | 134.0331
Reconstruction speed
21

## Slide 22
Chart: Relative reconsturction time compared to Titan X
| Titan X | GTX 980 | Titan Z (1 GPU) | Titan Z (2GPU) | Titan Black | GTX 690 (1GPU) | GTX 690 (2GPU)
HUCT | 1 | 1.2255 | 1.7096 | 0.94506 | 1.4696 | 2.9571 | 1.5071
Measurements
Titan X speedup
22

## Slide 23
Thank you for your attention!
23
Notes: 23