## Slide 1: The Role of Catalysis in Chemical Energy Storage
MTA EK, 2015.05.04.
József Sándor Pap Surface Chemistry and Catalysis Department
Notes: 1

## Slide 2
Renewable energy sources –how to store the produced energy?
Israel – 10 MW solar thermal pp.
(with backup biomass facility)
Wind turbines – low energy density
Japan – 30 MW offshore solar pp.
Renewables are either
INTERMITTENT
DIFFUSE or
LOW DENSITY!

## Slide 3
Renewable energy sources –how to store the produced energy?
"Getting battery cost down is key, but on the stationary storage side there is a lot of questions about which chemistry will dominate long term. It might not be lithium…”
- Colin Langan at UBS on Tesla’s announcement of Powerwall Li batteries

## Slide 4: Energy density becomes decisive when it comes to applications
G. Centi, et al. in Catalysis for Alternative Energy Generation,
Eds. L. Guczi and A. Erdőhelyi, Springer (2012)
ESSENTIALS…
Appropriate volumetric AND gravimetric energy density.
Ease of storage (C-based).
Less toxic, safety of precesses.
Can be used with the existing technologies for fossils.
Low environmental impact (both production and use).

## Slide 5
Hydrogen economy
(an attractive way to store
and distribute energy)

## Slide 6: Analogy to fossil fuels – long ago stored energy of sunlight
Hydrocarbons
DHr° = -890 kJ/mol
Cons:
- CO2 emission
- Finite sources
- efficiency limits
(power plants and engines)
- Air pollution
DHr° = -286 kJ/mol
Hydrogen
Pros:
- Cheap access
- Cheap storage, process and distribution
- Optimal energy density
- Established technologies
(power plants and internal combustion engines)
- Accepted by society
43 % percent of current energy usage comes from fossils!

## Slide 7: Role of H2 today – production and use
Steam reforming of nat. gas or naphta
Partial oxidation of heavy oil
Benzine reforming
Coal gasification
Synthesis of ethene
Chlor-alkali industry
Other
Water electrolysis
Synthesis of ammonia
Process heat generation
Processing of mineral oil
Benzine reforming
Fisher-Tropsch synthesis
Other
(oxo synth.,
hydrogenation, reductions)
109 m3N
190
120
90
50
33
10
7
1,3
109 m3N
200
150
25
15
10
Encyclopedia of Electrochemistry, Vol. 5: Electrochemical Engineering, Wiley (2007)
Production
Consumption
100
H YD R O G EN
Only 0.25% of hydrogen is produced by electrolysis.
…because it is profitable only when electric power is cheap.
Privileged attention to water electrolysis comes with the hydrogen economy concept.

## Slide 8: Use of H2 (or derived products) as energy carrier
Fuel cells
Methanol fuel cells
liquid H2 carriers
Surya Prakash & Oláh György (1990)
The key to efficiency and to pay-off is CATALYSIS!

## Slide 9
Brown-H2 example: reforming - net carbon reduction of 30%.
Green-H2 example: electrolysis renewable - emissions-free.
- 2015
2015-2020
2020-2030
Natural Gas
Reforming
Water
Electrolysis
(grid)
Bio-Derived
Liquids
Reforming
Coal
Gasification
(no carbon capture)
Ethanol
Reforming
Biomass
Gasification
Coal
Gasification
(carbon capture)
Water
Electrolysis
(wind)
Water
Electrolysis
(solar)
Distributed
Central
Photo-
Electro-
chemical
Biological
Thermo-
Chemical*
High-Temp.
Water Electrolysis*
10
1,000
10,000
50,000
100,000
100,000,000
Capacity (kg/day)
Target: 0.15 € / kWh
*either solar or nuclear
Production of H2 (or derived products) as energy carrier

## Slide 10: A considerable advantage of H2 over CHs
Electrochemistry! Water electrolysis can be directly
connected with renewable power plants!

## Slide 11
What is water oxidation and why is it important?
WOC: water oxidation catalyst,
a compound that can accelerate the evolution of O2 from water and can be attached to electrode surface.

## Slide 12
Self-organized metal oxides and hydroxides

## Slide 13
Photosensitized supramolecular systems

## Slide 14
Homogeneous catalysts: stability (104>TON), sensitivity (anions, contaminants)
Heterogeneous catalysts: rate (small TOF), deactivation (nano)
Electrocatalysts: overpotential
homogeneous: 0,6-0,9 V
heterogeneous: 0,2-0,4 V
Photocatalysts:
small quantum efficiency in the visible range of activation
There is plenty of space for further research, because…

## Slide 15
…and studies in
our laboratory

## Slide 16
Sc | Ti | V | Cr | Mn | Fe | Co | Ni | Cu | Zn
Y | Zr | Nb | Mo | Tc | Ru | Rh | Pd | Ag | Cd
La | Hf | Ta | W | Re | Os | Ir | Pt | Au | Hg
Transition metals that are cheap, abundant, have more available oxidation states.
AIM: studying
supramolecular systems that in part
exploit molecular catalysts and carry potential
to merge advantages of the different approaches.
Three directions:
(1) Ru-based catalysts and related metal-organic frameworks,
(2) Cu complexes for electrocatalysis
(3) Photosensitized layered double hydroxides (LDHs) for photo(electro)catalysis.
Considerations

## Slide 18
MOFs
Molecular catalysts
Ru-based MOFs
Problem:
ligand dissociation leads to rapid deactivation
Advantage:
complexes with no open sites are the most active catalysts
Problem:
the lack of open sites bottlenecks catalytic applications
Advantage:
porous materials, existing options for surface anchoring (SURMOF)

## Slide 19
Layered double hydroxides (LDH) [M’(II)1-xM(III)x(OH)2]x+[Am-x/m•nH2O]x-
- M’(II) and M(III) are variable
- rM’(II) ≈ rM(III)
- Surface adsorbed water
- Weakly bound water
- Strogly bound water
- Intercalation options
Heat induces reversible
changes (memory effect)
Photosensitized LDHs with abundant metals
Small molecule
photosensitizer

## Slide 20
Thank you for attention!
Köszönöm a figyelmet!